# Appendix
## ICB-S-RJ-2016-##, Rev 0.6 and Rev 0.7
### Partslist (may vary on subsequent or previous Revisions)
Part	Value	Layer	Description
J1		Top	RJ45-Connector, 8pin, vertical
J2		Top	dto., Input or Output of RS-485-Bus
C1	22uF	Top	Tantal ElCo, Ripple Rejection 12V adj	1206
C2	100nF	Top	CerCo Ripple Rejection 5V VCC Max487	1206
C3	10uF	Top	Stabilizer Input AMS1117adj	0805
C4	10uF	Top	Stabilizer Input AMS1117 5.0	0805
C5	22uF	Top	Tantal ElCo, Ripple Rejection 5.0 V	1206
P1	5x2mm	Top	12V receptacle
U1	AMS1117adj	Top	provides 0 ... 12V for Backlight(BLT)-Trim	gets hot, maybe
U2	AMS1117 5.0	Top	provides 5.0 Volts for Max487
U3	Max487	Top	RS-485-Transmitter
U4	PC357	Top	Optocoupler	obsolete at later Revs
U5	IRLR024	Top	MOSFET n-Channel PWM-Backlight	D-Pak
TP1/TP2	Pads	Top	Testpoints for Trobleshooting RS-485-Bus Lanes A and B	obsolete at later Revs
R1	Pot 1k linear	Top	Backlight-Tim
R2	120R	Top	Backlight-Trim	0805
R3	820R	Top	Monitoring Backlight	0805
R4	820R	Top	Monitoring 5.0 Volt	0805
R5	220R	Top	controlling PWM Backlight	1206
R6	100k	Top	controlling PWM, pull down Gate	1206
R7	10k	Top	pull down, TXenable	1206
R8	10k	Top	controlling PWM, pull down Gate	1206
R9	2k7	Top	controlling PWM, Gate	1206
D1	LED	Top	Monitoring Backlights	1206
D2	LED	Top	Monitoring 5.0 Volt	1206
D3	SMBJ12A	Back	TVS 12V Main Supply	SMB
D4	SMBJ12A	Back	TVS 12V external Supply	SMB
D5	SM712	Back	TVS RS-485-Lines	SOT-23
D6	MBRS320	Back	Schottky, automatic Power-Selector 3 A	SMC
J3	2x3 (fe)male	Back	12V supply OUT
J4	1x3 female	Back	12V PWM-OUT for Backlight
J5/J6	1x15 female	Top	Socket for Arduino NANO
J7	1x20 male	Back	digital I/O D4...D13	see Table 2 and 3
J8	1x20 male	Back	analog IN A0...A6	see Table 2 and 3
F1	PTC	Back	12V/ 2.5 A self-resettable Fuse

overall size of the PCB: 120 mm x 58 mm
Coordinates of mounting holes (lower left corner is 0/0): 6/54, 114/54, 6/5, 114/5
### Pin-Outs (just valid to Revision 0.6 and 0.7)
Connector	Pin-Count	Pin	Function
J1/J2	Bottom Layer, Down-Right is Pin 1 Top-Right is Pin 2	1	RS 485 A, IN/OUT
		2	RS 485 B, IN/OUT
		3, 4, 6, Shield	GND
		5, 7, 8	12V+ IN/OUT, 1A per Lane
J3	Bottom-Layer / Top-Right is Pin 1 / Top-Left is Pin 2	2, 4, 6 / (left Column)	12V+ OUT / direct connection to P1 (external, additional 12V supply)
		1, 3, 5	GND
P1	Center is Pin 1	1	12V+ IN
		2	GND
J4	Top is Pin 1	1, 3	-12V* PWM (Drain of MOS-FET U5)
		2	+12V, max. 1,0 A, / regulated/controlled by AMS1117-Adj
J5/J6	Top-Layer / Top-Right is 1 / Top-Left is 15		Common Arduino NANO / Attention: stack NANO at correct position
J7	Bottom-Layer / Top-Left is 1	2, 4, 6, 8, 10, 12, 14, 16, 18, 20	GND
		1	D4 (digital I/O)
		3	D5 (digital I/O)
		5	D6 (digital I/O)
		7	D7 (digital I/O)
		9	D8 (digital I/O)
		11	D9 (digital I/O)
		13	D10 (digital I/O)
		15	D11 (digital I/O)
		17	D12 (digital I/O)
		19	D13 (digital I/O)
J8	Bottom-Layer / Top-Right is 1	1, 4, 7, 10, 13, 16, 20	GND (pay Attention: not every even/odd Pin-Number)
		2	A0 (analog or digital Input)
		5	A1 (analog or digital Input)
		8	A2 (analog or digital Input)
		11	A3 (analog or digital Input)
		14	A4 (analog or digital Input)
		17	A5 (analog or digital Input)
		19	A6 (analog or digital Input)
		3, 6, 9, 12, 15, 18	5,0 V for driving analog Pots, / provided by NANO on board AMS.

### Same Pin-Outs in physical Order
##### (just valid to Revision 0.6 and 0.7)
J7			J8
Pin (left to right)	Function		Pin (right to left)	Function
1	D4		1	GND
2	GND		2	A0
3	D5 (PWM)		3	5.0 V
4	GND		4	GND
5	D6 (PWM)		5	A1
6	GND		6	5.0 V
7	D7		7	GND
8	GND		8	A2
9	D8		9	5.0 V
10	GND		10	GND
11	D9 (PWM)		11	A3
12	GND		12	5.0 V
13	D10 (PWM)		13	GND
14	GND		14	A4
15	D11 (PWM)		15	5.0 V
16	GND		16	GND
17	D12		17	A5
18	GND		18	5.0 V
19	D13		19	A6
20	GND		20	GND